Team Meeting Record Sheet

	Date: August 12, 2025	Participator: Supervisor Huang, Engineer Ben and me.
1	IR Camera 640*512 Resolution / (Optical Fiber Supply Version)	Put Hirose70239 Adapter PCB to fabrication. / Limited by available pins of Hirose39 on DPU board, only CDS3 Interface is supported. / Debug and prepare one piece to engineer Ben after PCB comes back.
Progress, PCBA is ongoing.
2	Mechanical case with a power supply switch. / (Lithium Battery Version)	Prepare a mechanical case with soldering a power supply switch, therefore the worker turns on switch after installing it on power tower to only acquire a frame saved in Hyper RAM, read back by sending a command via UART.
I tested DPU with a lab power supply, it can run at 3.7V input. A lithium battery sources 4.2V when full charged, discharges limit is 3.6V.
3	Assemble two x86 stations	Get assistance from Engineer Niu to assemble two x86 stations that can supply optics, and receive data from DPU. / Engineer Ben is charge of arranging CAD figure, get original design documents from WangAi.
Progress, two x86 station assembly completed, now Engineer Niu is installing optical components.